## Slide 1: TỔNG QUAN VỀ FIREWALL
Nguyễn Văn Bình

## Slide 2: Firewall là gì?
Outside
Network
DMZ
Network
Inside
Network
Internet
A firewall is a system or group of systems that manages access between two or more networks.

## Slide 3: Các kỹ thuật trong Firewall
Firewall operations are based on one of these technologies:
  Packet filtering (ACL)
  Stateful packet filtering (Stateful FW)
  Proxy server (Web Proxy Server)
  Next Generation Firewall (AV, IDS/IPS)

## Slide 4: Kỹ thuật Packet Filtering
Limits information that is allowed into a network based on the destination and source address

## Slide 5: Kỹ thuật Stateful Packet Filtering
172.16.0.50
10.0.0.11
1026
80
49091
Syn
172.16.0.50
192.168.0.20
49769
Syn
1026
80
Source port
Destination address
Source address
Initial sequence no.
Destination port
Flag
Ack
State Table
Limits information that is allowed into a network based not only on the destination and source addresses, but also on the packets state table content

## Slide 6: Kỹ thuật Proxy Server
Outside
Network
Proxy
Server
Inside
Network
Internet
Requests connections on behalf of a client

## Slide 7: Next Generation FW

## Slide 8: Các tính năng của Firewall
Some features of security appliances are:
  Proprietary operating system
  Stateful packet inspection
  User-based authentication
  Protocol and application inspection
  Modular policy framework
  Virtual private networking
  Security contexts (virtual firewalls)
  Stateful failover capabilities
  Transparent firewalls
  Web-based management solutions

## Slide 9: Tính năng Stateful Packet Inspection
  The stateful packet inspection algorithm provides stateful connection security.
    It tracks source and destination ports and addresses, TCP sequence numbers, and additional TCP flags.
    It randomizes the initial TCP sequence number of each new connection.
  By default, the stateful packet inspection algorithm allows connections originating from hosts on inside (higher security level) interfaces.
  By default, the stateful packet inspection algorithm drops connection attempts originating from hosts on outside (lower security level) interfaces.
  The stateful packet inspection algorithm supports authentication, authorization, and accounting.

## Slide 10: Tính năng Application-Aware Inspection
FTP
Server
Client
Control
Port
2008
Data
Port
2010
Data
Port 20
Control
Port
21
Data - Port 2010
Port 2010 OK
Data
  Protocols such as FTP, HTTP, H.323, and SQL*Net need to negotiate connections to dynamically assigned source or destination ports through the firewall.
  The security appliance inspects packets above the network layer.
  The security appliance securely opens and closes negotiated ports for legitimate client-server connections through the firewall.

## Slide 11: Tính năng Modular Policy
Headquarters
System Engineer
Site B
Executives
Site C
T1
Internet
SE
exec
S2S
S2S
Internet
Class Map
Traffic Flow
Default
Internet
Systems Engineer
Executives
Site to Site
Policy Map
Services
Inspect
IPS
Police
Priority
Service Policy
Interface/Global
Global
Outside

## Slide 12: Tính năng Virtual Private Network
B A N K
Site to Site
Remote Access
IPsec VPN
SSL VPN
Internet
B A N K
Headquarters

## Slide 13: Tính năng Security Context (Virtual Firewall)
Four Physical Firewalls
One Physical Firewall
Four Virtual Firewalls
Internet
Internet
  Ability to create multiple security contexts (virtual firewalls) within a single security appliance

## Slide 14: Tính năng Failover
Primary:
Failed Firewall
Secondary:
Active Firewall
Internet
Failover: Active/Standby
Primary:
Failed/Standby
Failover: Active/Active
Secondary:
Active/Active
Internet
Contexts
Failover protects the network if the primary security appliance goes offline..
    Active/standby: Only one unit can be actively processing traffic; the other is hot standby.
    Active/Active: Both units can process traffic and serve as backup units.
Stateful failover maintains the operating state during failover.
2
1
2
1

## Slide 15: Tính năng Web-Based Management
Adaptive
Security
Device
Manager

## Slide 16: Thảo luận