## Slide 1: HƯỚNG DẪN CẤU HÌNH FIREWALL CISCO ASA
Nguyễn Văn Bình

## Slide 2: PHẦN 1
Cisco Security Appliances
Overview

## Slide 3: Các dòng Firewall Cisco ASA 5500
SMB
Price
Functionality
Gigabit Ethernet
Enterprise
ROBO
SOHO
SP
ASA 5520
ASA 5540
ASA 5510
ASA 5550 - 5580
ASA 5505
SP = service provider

## Slide 4: Cisco ASA 5510 Adaptive Security Appliance
  Delivers advanced security and networking services, including high-performance VPN services, for small and medium-sized businesses and enterprise branch offices
  Provides up to 130,000 concurrent connections
  Provides up to 300-Mbps firewall throughput
  Provides interface support
    Up to 5 10/100 Fast Ethernet interfaces
    Up to 25 VLANs
    Up to 5 contexts
  Supports failover
    Active/standby
  Supports VPNs
    Site to site (250 peers)
    Remote access
    WebVPN
  Supports optional SSMs (Cisco ASA AIP SSM, Cisco ASA CSC SSM, and four-port Gigabit Ethernet SSM)

## Slide 5: Cisco ASA 5520 Adaptive Security Appliance
  Delivers advanced security services, including high-performance VPN services, for medium-sized enterprise networks
  Provides up to 280,000 concurrent connections
  Provides up to 450-Mbps firewall throughput
  Provides Interface support
    4 10/100/1000 Gigabit Ethernet interfaces
    1 10/100 Fast Ethernet interface
    Up to 100 VLANs
    Up to 20 contexts
  Supports failover
    Active/standby
    Active/active
  Supports VPNs
    Site to site (750 peers)
    Remote access
    WebVPN
  Supports optional SSMs (Cisco ASA AIP SSM, Cisco ASA CSC SSM, and four-port Gigabit Ethernet SSM)

## Slide 6: Cisco ASA 5540 Adaptive Security Appliance
  Delivers high-performance, high-density security services, including high-performance VPN services, for medium-sized and large enterprise networks and service provider networks
  Provides up to 400,000 concurrent connections
  Provides up to 650-Mbps firewall throughput
  Provides Interface support
    4 10/100/1000 Gigabit Ethernet interfaces
    1 10/100 Fast Ethernet interface
    Up to 200 VLANs
    Up to 50 contexts
  Supports failover
    Active/standby
    Active/active
  Supports VPNs
    Site to site (5,000 peers)
    Remote access
    WebVPN
  Supports optional SSMs (Cisco ASA AIP SSM, Cisco ASA CSC SSM, and four-port Gigabit Ethernet SSM)

## Slide 7: ASA 5510, 5520, and 5540 Adaptive Security Appliances Front Panel
Power
Status
Active
Flash
VPN

## Slide 8: ASA 5510, 5520, and 5540 Adaptive Security Appliances Back Panel
Security services
module
Fixed interfaces
CompactFlash

## Slide 9: ASA 5510, 5520, and 5540 Adaptive Security Appliances Connectors
Four 10/100/1000
Gigabit Ethernet ports*
10/100 out-of-band
management port
AUX ports
CompactFlash
Two USB 2.0 ports
Power supply
(AC or DC)
Console
port
*ASA 5510 Adaptive Security Appliance supports 10/100 Fast Ethernet ports.

## Slide 10: Cisco ASA Security Services Module
  High-performance module designed to provide additional security services
  Diskless (Flash-based) design for improved reliability
  Gigabit Ethernet port for out-of-band management

## Slide 11: Four-Port Gigabit Ethernet SSM
RJ-45 link
LED
RJ-45
speed
LED
SFP link
LED
SFP
speed
LED
RJ-45
ports
Power
LED
Status
LED
SFP
ports

## Slide 12: SSM Models
Power
Status
Speed
Link and activity
  SSM-10
    2.0-GHz processor
    1.0 GB RAM
  SSM-20
    2.4-GHz processor
    2.0 GB RAM

## Slide 13: PHẦN 2
Getting Started with Cisco Security Appliances

## Slide 14: Security Appliance Access Modes
ciscoasa>
ciscoasa#
ciscoasa(config)#
monitor>
A Cisco security appliance has four main administrative access modes:
  Unprivileged
  Privileged
  Configuration
  Monitor

## Slide 15: Access Privileged Mode
ciscoasa> enable
password:
ciscoasa#
enable [priv_level]
ciscoasa>
  Used to control access to the privileged mode
  Enables you to enter other access modes
Internet

## Slide 16: Access Configuration Mode
configure terminal
ciscoasa#
  Used to start configuration mode to enter configuration commands from a terminal
ciscoasa> enable
password:
ciscoasa# configure terminal
ciscoasa(config)# exit
ciscoasa# exit
ciscoasa>
exit
ciscoasa#
  Used to exit from an access mode

## Slide 17: Viewing and Saving Your Configuration
The following commands enable you to view your configuration:
  Show running-config
  Show startup-config
The following commands enable you to save your configuration:
  copy run start
  write memory
To save configuration changes:
copy run start
running-
config
startup-
config
(saved)
Configuration
Changes

## Slide 18: Erase Startup Configuration
ciscoasa#
write erase
Clear the Startup configuration:
running-
config
(default)
startup-
config

## Slide 19: Reload the Configuration
  Reboots the security appliance and reloads the configuration
  Allows scheduled reboots
ciscoasa# reload
Proceed with reload?[confirm] y
Rebooting...
reload [at hh:mm [month day | day month]] [cancel] [in [hh:]mm] [max-hold-time [hh:]mm] [noconfirm] [quick] [reason text] [save-config]
ciscoasa#

## Slide 20: Displaying Stored Files
  Display the directory contents
ciscoasa#
ASA
disk0:
disk1:
ciscoasa# dir
Directory of disk0:/
8 -rw- 8202240 13:37:33 Jul 28 2006 asa721-k8.bin
1264 -rw- 5539756 13:21:13 Jul 28 2006 asdm-521.bin
62947328 bytes total (49152000 bytes free)
dir [/all] [/recursive] [all-filesystems] [disk0: | disk1: | flash: | system:]
Internet

## Slide 21: show commands
show run interface
show interface
Show interface ip brief
show memory
show cpu usage
show version
show ip address
show nameif
show run nat
show run global
show xlate
show route
10.0.1.11
10.0.1.4
10.0.1.X
X.X.X.X
NAT
Internet
Mapped Pool
192.168.1.20-192.168.1.254
10.0.1.11
10.0.1.4
10.0.1.X
Internet

## Slide 22: PHẦN 3
Appliance Access Management

## Slide 23: Assigning a Hostname
  Changes the hostname in the security appliance CLI prompt
ciscoasa(config)#
ciscoasa(config)# hostname asa1 asa1(config)#
hostname newname
New York ( asa1)
Server
Boston
(asa2)
Server
Server
Dallas
(asa3)
Internet

## Slide 24: Configuring Remote Access Password
asa1(config)# passwd telnetpass
  Sets the password for Telnet access to set the security appliance
passwd password [encrypted]
ciscoasa(config)#
10.0.0.11
Telnet
Internet
password: telnetpass

## Slide 25: Configuring Enable (Privileged) Password
ciscoasa(config)# enable password mysecretpassword
  Sets the password for Privileged mode
enable password password
ciscoasa(config)#
10.0.0.11
Internet

## Slide 26: Configuring Telnet Access
telnet {{hostname | IP_address mask interface_name} | {IPv6_address interface_name} | {timeout number}}
ciscoasa(config)#
asa1(config)# telnet 10.0.0.11 255.255.255.255 inside
asa1(config)# telnet timeout 15
asa1(config)# passwd telnetpass
  Enables you to specify which hosts can access the security appliance console with Telnet and set the maximum time a console Telnet session can be idle before being logged off by the security appliance
  Sets the password for Telnet access to set the security appliance
passwd password [encrypted]
ciscoasa(config)#
10.0.0.11
Telnet
Internet

## Slide 27: Configuring SSH Access
crypto key zeroize {rsa | dsa} [label key-pair-label] [default] [noconfirm]
  Removes any previously generated RSA keys
ciscoasa(config)#
  Saves the CA state
write memory
ciscoasa(config)#
  Configures the domain name
domain-name name
ciscoasa(config)#
  Generates an RSA key pair
crypto key generate rsa [usage-keys | general-keys] [label key-pair-label] [modulus size] [noconfirm]
ciscoasa(config)#
  Specifies the host or network authorized to initiate an SSH connection
ssh {ip_address mask | ipv6_address/prefix} interface
ciscoasa(config)#
  Specifies how long a session can be idle before being disconnected
ssh timeout number
ciscoasa(config)#

## Slide 28: Configuring SSH Access Example
asa1(config)# crypto key zeroize rsa
asa1(config)# write memory
asa1(config)# domain-name cisco.com
asa1(config)# crypto key generate rsa modulus 1024
asa1(config)# write memory
asa1(config)# ssh 172.26.26.50 255.255.255.255 outside
asa1(config)# ssh timeout 30
172.26.26.50
SSH
username: pix
password: telnetpassword
Internet

## Slide 29: Configuring User Authentication
ciscoasa(config)#username ciscoadmin password adminpassword privilege 15
  Creates user account
username username {nopassword | password} password
[encrypted] [privilege privilege_level]
ciscoasa(config)#
  Enables authentication for appliance access controlling
aaa authentication {serial | enable | telnet | ssh | http} console {AAA_group_tag | [LOCAL]}
ciscoasa(config)# aaa authentication ssh console LOCAL
ciscoasa(config)# aaa authentication http console LOCAL
ciscoasa(config)# ssh 10.0.1.0 255.255.255.0 inside
ciscoasa(config)# http 10.0.1.0 255.255.255.0 inside

## Slide 30: PHẦN 4
Basic Security Appliance Configuration

## Slide 31: Interface Name & Security Level
Outside Network
GigabitEthernet0/0
Security level 0
Interface name = outside
DMZ Network
GigabitEthernet0/2
Security level 50
Interface name = DMZ
Inside Network
GigabitEthernet0/1
Security level 100
Interface name = inside
g0/0
g0/2
g0/1
Internet

## Slide 32: interface Commands
interface {physical_interface[.subinterface] | mapped_name}
ciscoasa(config)#
asa1(config)# interface GigabitEthernet0/0
asa1(config-if)#
  Enters configuration mode for the interface you specify
GigabitEthernet0/0
GigabitEthernet0/2
GigabitEthernet0/1
g0/0
g0/2
g0/1
Internet

## Slide 33: Assign an Interface Name
nameif if_name
ciscoasa(config-if)#
asa1(config)# interface GigabitEthernet0/0
asa1(config-if)# nameif outside
  Assigns a name to an interface on the security appliance.
GigabitEthernet0/2
Interface name = dmz
GigabitEthernet0/0
Interface name = outside
GigabitEthernet0/1
Interface name = inside
g0/0
g0/2
g0/1
Internet

## Slide 34: Assign a Security Level
security-level number
ciscoasa(config-if)#
  Assigns a security level to the interface
asa1(config)# interface GigabitEthernet0/0
asa1(config-if)# nameif outside
asa1(config-if)# security-level 0
GigabitEthernet0/0
Interface name = outside
IP address = 192.168.1.2
Security level = 0
g0/0
g0/2
g0/1
Internet

## Slide 35: Interfaces with Same Security Level
  Enables communication between interfaces with the same security level or allows traffic to enter and exit the same interface
ciscoasa(config)#
asa1(config)# same-security-traffic permit inter-interface
same-security-traffic permit {inter-interface | intra-interface}
DMZ Network
GigabitEthernet0/2
Security level 100
Interface name = dmz
g0/0
g0/2
g0/1
Internet
Inside Network
GigabitEthernet0/1
Security level 100
Interface name = inside

## Slide 36: Assign Interface IP Address
ip address ip_address [mask] [standby ip_address]
ciscoasa(config-if)#
  Assigns an IP address to each interface
asa1(config)# interface GigabitEthernet0/0
asa1(config-if)# nameif outside
asa1(config-if)# security-level 0
asa1(config-if)# ip address 192.168.1.2 255.255.255.0
GigabitEthernet0/0
Interface name = outside
IP address = 192.168.1.2
g0/0
g0/2
g0/1
Internet

## Slide 37: Assign an Interface Speed and Duplex
speed {10 | 100 | 1000 | auto | nonegotiate}
duplex {auto | full | half}
  Enable the interface speed and duplex
ciscoasa(config-if)#
GigabitEthernet0/0
Speed =1000
Duplex = full
g0/0
g0/2
g0/1
Internet
asa1(config)# interface GigabitEthernet0/0
asa1(config-if)# nameif outside
asa1(config-if)# ip address 192.168.1.2
asa1(config-if)# security-level 0
asa1(config-if)# speed 1000
asa1(config-if)# duplex full

## Slide 38: ASA Management Interface
management-only
ciscoasa(config-if)#
  Disables management-only mode (for ASA 5520, 5540 and 5550)
asa1(config)# interface management0/0
asa1(config-if)# no management-only
no management-only
  Configures an interface to accept management traffic only
  Disables management-only mode
Management0/0
Management only = no
g0/0
g0/2
g0/1
Internet
m0/0

## Slide 39: Enabling and Disabling Interfaces
  Disables management-only mode (for ASA 5520, 5540 and 5550)
asa1(config)# interface GigabitEthernet0/0
asa1(config-if)# no shutdown
shutdown
  Disables an interface
  no shutdown = enabled
ciscoasa(config-if)#
GigabitEthernet0/0
Enabled
g0/0
g0/2
g0/1
Internet

## Slide 40: Configure a Static Route
route if_name ip_address netmask gateway_ip [metric]
ciscoasa(config)#
  Defines a static or default route for an interface
asa1(config)# route outside 0.0.0.0 0.0.0.0 192.168.1.1 1
asa1(config)# route inside 10.1.1.0 255.255.255.0 10.0.1.102 1
192.168.1.1
10.1.1.11
10.1.1.4
Default Route
10.0.1.102
Static Route
Internet

## Slide 41: DHCP Server
dhcpd address 10.0.1.101-10.0.1.110 inside
dhcpd dns 8.8.8.8 8.8.4.4
dhcpd lease 3000
dhcpd enable inside
dhcpd option 3 ip 10.0.1.1
GigabitEthernet0/1
Interface name = inside
IP address = 10.0.1.1
g0/1
DHCP
Assigned
Internet
show dhcpd binding all

## Slide 42: Configuration Example
  asa1(config)# write terminal
  . . .
  interface GigabitEthernet0/0
  speed 1000
  duplex full
  nameif outside
  security-level 0
  ip address 192.168.1.2 255.255.255.0
  interface GigabitEthernet0/1
  speed 1000
  duplex full
  nameif inside
  security-level 100
  ip address 10.0.1.1 255.255.255.0 . . .
GigabitEthernet0/0
Interface name = outside
Security level = 0
IP address = 192.168.1.2
GigabitEthernet0/1
Interface name = inside
Security level = 100
IP address = 10.0.1.1
172.16.1.0
.1
10.0.1.0
.1
192.168.1.0
.2
10.1.1.0
.1
Internet

## Slide 43: Configuration Example (Cont.)
  interface GigabitEthernet0/2
  nameif dmz
  security-level 50
  speed 1000
  duplex full
  ip address 172.16.1.1 255.255.255.0
  passwd 2KFQnbNIdI.2KYOU encrypted
  hostname asa1
  names
  name 172.16.1.2 bastionhost
  name 10.1.1.11 insidehost
172.16.1.0
.1
10.0.1.0
.1
192.168.1.0
.2
10.1.1.0
.1
GigabitEthernet0/2
Interface name = dmz
Security level = 50
IP address = 172.16.1.1
“insidehost”
10.1.1.11
“bastionhost”
172.16.1.2
Internet

## Slide 44: Configuration Example (Cont.)
  route outside 0.0.0.0 0.0.0.0 192.168.1.1 1
  route inside 10.1.1.0 255.255.255.0 10.0.1.102 1
172.16.1.0
.2
.1
.102
“insidehost”
10.1.1.11
“bastionhost”
172.16.1.2
10.0.1.0
.1
192.168.1.0
.2
.1
10.1.1.0
.1
Default Route
Static Route
Internet

## Slide 45: PHẦN 5
Advanced Security Appliance Configuration

## Slide 46: access-list Command
  Permits outside HTTP traffic to access the public web server
asa1(config)# access-list ACLOUT permit tcp any host 192.168.1.9 eq www
192.168.1.0
10.0.1.0
Public Web Server
DMZ
Inside
Outside
.2
.1
192.168.1.9
172.16.1.2
Permit
Inbound
HTTP
Internet

## Slide 47: access-group Command
192.168.1.0
10.0.1.0
Public Web
Server
DMZ
Inside
Outside
.2
.1
  Applies an ACL to an interface
asa1(config)# access-group ACLOUT in interface outside
Apply ACL
to interface
ciscoasa(config)#
access-group access-list {in | out} interface interface_name [per-user-override]
Internet

## Slide 48: Object, Object-group & ACL
object network HQ_NET subnet 192.168.10.0 255.255.255.128 object network HQ_SERVER host 192.168.20.10
!
object-group network HQ_NETWORK network-object object HQ_NET
network-object object HQ_SERVER
network-object host 192.168.3.1
!
access-list HTTP_TO_HQ permit tcp any object-group HQ_NETWORK eq 80

## Slide 49: Object & NAT
object network WEB_SERVER
host 10.2.2.33
nat (inside,outside) static 73.8.2.33
object network INSIDE
subnet 10.6.6.0 255.255.255.0
nat (inside,outside) dynamic interface

## Slide 50: Static NAT: (One to One)
1. Create object group.
2. Define object IP address.
3. Create NAT statement within object group.
4. Create access-list
5. Assign access-group to interface
object network WEB_SERVER
host 192.168.3.10
nat (DMZ,outside) static 210.130.3.5
access-list OUTSIDE extended permit tcp any host 210.130.3.5 eq 80
access-group OUTSIDE in interface outside

## Slide 51: Dynamic NAT: (Many to One)
1. Create object group.
2. Define object IP address.
3. Create NAT statement within object group.
4. Create access-list
5. Assign access-group to interface
object network INSIDE_LAN
subnet 192.168.2.0 255.255.255.0
nat (inside,outside) dynamic interface
access-list standard INSIDE permit ip 192.168.2.0 0.0.0.255
access-group INSIDE in interface inside

## Slide 52: Port Forwarding
1. Create object group.
2. Define object IP address.
3. Create NAT statement within object group.
4. Create access-list
5. Assign access-group to interface
access-list OUTSIDE_IN extended permit tcp any host 192.168.3.10 eq 80
access-list OUTSIDE_IN extended permit tcp any host 192.168.3.10 eq 21
access-group OUTSIDE_IN in interface outside
object group WWW_SERVER
host 192.168.3.10
nat (DMZ,outside) static 210.130.3.4 service tcp 80 80
object group FTP_SERVER
host 192.168.3.11
nat (DMZ,outside) static 210.130.3.4 service tcp 21 21

## Slide 53: Allow ICMP
access-list OUTSIDE_IN extended permit icmp any any echo-reply
access-list OUTSIDE_IN extended permit icmp any any unreachable
access-list OUTSIDE_IN extended permit icmp any any time-exceeded
access-group OUTSIDE_IN in interface outside
  access-list OUTSIDE_IN extended permit icmp any any
  access-group OUTSIDE_IN in interface outside
Outside
Inside
ICMP Echo, Unreachable, time-exceeded
Internet

## Slide 54: PHẦN 6
ASDM Overview and Operating Requirements

## Slide 55: What Is ASDM?
ASDM is a browser-based configuration tool designed to help configure and monitor your security appliance.
Internet
SSL Secure Tunnel

## Slide 56: Supported Platforms
  Windows
  Sun Solaris
  Linux

## Slide 57: Running ASDM
Run ASDM as a:
  Local application
  Java applet
Launch Startup Wizard

## Slide 58: ASDM Home Window
Main toolbar
Device
Information
General
License
VPN Status
System
Resources
Interface
Status
Traffic
Status
Menu bar
Syslog
Messages

## Slide 59: ASDM Home Window (Cont.)
  License tab

## Slide 60: Startup Wizard
Startup Wizard
  Interfaces
  NAT and PAT
  Hostname
  Domain name
  Enable password

## Slide 61: VPN Wizard
VPN Wizard
  Site-to-Site
  Remote Access
Note: Use Configuration > VPN to edit VPN connections.

## Slide 62: High Availability and Scalability Wizard
High Availability and Scalability Wizard
  Active/Active Failover
  Active/Standby Failover
  VPN Cluster Load Balancing

## Slide 63: Configuration Window
Configuration
  Interface
  Security Policy
  NAT
  VPN
  IPS or
  CSD Manager
  Routing
  Global Objects
  Properties

## Slide 64: Interfaces
  IP address
    Static
    DHCP
  Same security level

## Slide 65: Security Policy
  Access Rules
  AAA Rules
  Filter Rules
  Service Policy Rules

## Slide 66: NAT
  Translation Rules
    NAT
    Policy NAT
    NAT exemption
    Maximum connections
    Embryonic connections
  NAT0

## Slide 67: VPN
Edit VPN
  General
  IKE
  IPsec
  IP Address Management
  Load Balancing
  NAC
  WebVPN
  E-Mail Proxy
Note: Use the Remote Access or Site-to-Site VPN Wizard for new VPN connections.

## Slide 68: Routing
  Static Routes
  Dynamic Routing
    OSPF
    RIP
  Multicast
    IGMP
    MRoute
    PIM
  Proxy ARPs

## Slide 69: Global Objects
  Network Object Groups
  IP Names
  Service Groups
  Class Maps
  Inspect Maps
  Regular Expressions
  TCP Maps
  Time Ranges

## Slide 70: Monitoring Button
  Interfaces
  VPN
  IPS or Trend Micro Content Security
  Routing
  Properties
  Logging

## Slide 71: Interface Graphs Panel
The Interface Graphs panel enables you to monitor per-interface statistics, such as bit rates, for each enabled interface on the security appliance.

## Slide 72: Packet Tracer
Interface
Source IP
Source port
Destination IP
Destination port
Flow lookup
Route lookup
Access list

## Slide 73: Options > Preferences
Options

## Slide 74: Tools
Tools
  Command Line Interface
  Packet Tracer
  Ping
  Traceroute
  File Management
  Ugrade Software
  Upload ASDM Assistant Guide
  System Reload
  ASDM Java Console

## Slide 75: Thảo luận