## Slide 1
KHOA KỸ THUẬT MÁY TÍNH VÀ ĐIỆN TỬ
Đà nẵng, tháng 1 năm 2026
Nhân bản – Phụng sự – Khai phóng
GRADUATION THESIS
BUILDING AN ENTERPRISE NETWORK SYSTEM WITH AUTOMATION USING ANSIBLE, MONITORING WITH PROMETHEUS, AND SECURITY WITH PFSENSE IDS/IPS
Student Name: Nguyen An Phuc
Student ID: 21IT639
Supervisor: Dr. Dang Quang Hien

## Slide 2
OUTLINE
  Introduction & Objectives
  Core Technologies
  Network Topology Design
  System Data Flow
  System Implementation
  Experimental Results
  Evaluation & Future Development
  Conclusion
Faculty of Computer Engineering and Electronics
Page 2/18

## Slide 3
1. INTRODUCTION & OBJECTIVES
Faculty of Computer Engineering and Electronics
  Manual Administration: Time-consuming, prone to human errors during repetitive tasks.
  Lack of Centralized Monitoring: Difficult to identify the root cause of incidents; scattered data.
  Passive Security: Traditional routers/firewalls fail to prevent high-speed automated attacks.
1. Context & Challenges:
  Combining Network + DevOps (Infrastructure as Code).
  Automated Administration – Active Monitoring – Proactive Security.
  Infrastructure: Secure Network Zoning (DMZ, LAN, WAN).
  Automation: Automated Configuration Backup, Agent Deployment (Ansible, Python).
  Monitoring: Centralized Metrics & Logs (Prometheus, Grafana).
2. NetDevOps Solution:
3. Research Objectives:
Page 3/18

## Slide 4
2. CORE TECHNOLOGIES
  Ansible: Agentless configuration management, utilizing SSH.
  Teleport: Secure remote access, replacing traditional SSH, session recording.
Automation
Monitoring & Logging
Infrastructure & Security
  Prometheus: Metric collection (CPU, RAM, Traffic).
  Grafana: Data visualization (Dashboards).
  Loki & Promtail: Centralized log aggregation and querying.
  pfSense: Open-source Router/Firewall.
  Suricata: Intrusion Detection and Prevention System .
  Docker/GNS3: Virtualization and simulation environments.
Faculty of Computer Engineering and Electronics
Page 4/18

## Slide 5
3. NETWORK TOPOLOGY DESIGN
Page 2/16
  WAN: Internet Connection (NAT).
  DMZ: Public Services (Web, Mail, Proxy).
  LAN: Internal Users (Staff, Guest, Tech, Manager).
1. Zoning Architecture:
Faculty of Computer Engineering and Electronics
  pfSense: Central Gateway, Firewall, NAT, HAProxy, Suricata.
  Network Devices: Cisco L3/L2 Switches.
  Servers: Linux (Ubuntu/Debian).
2. Infrastructure Components:
Page 5/18

## Slide 6
4. SYSTEM DATA FLOW
Page 2/16
Faculty of Computer Engineering and Electronics
1. Monitoring Flow (Metric):
- Target (SNMP) -> Prometheus (Pull) -> Alertmanager.
2. Logging Flow (Logs):
- Device (Syslog) -> Promtail -> Loki (Storage).
3. Visualization Flow:
- User -> Grafana Dashboard -> Query Data.
4. Automation Flow:
- Ansible -> SSH -> Network Devices (Config/Backup).
Faculty of Computer Engineering and Electronics
Page 6/18

## Slide 7
5. NETWORK INFRASTRUCTURE & SECURITY IMPLEMENTATION
Page 2/16
  VLAN & Trunking: Network segmentation, 802.1Q Trunking.
  OSPF: Dynamic routing, automatic route updates.
  HSRP: Gateway Redundancy (Active/Standby), ensuring High Availability.
1. Switch Configuration (Cisco):
Faculty of Computer Engineering and Electronics
Page 7/18

## Slide 8
5. NETWORK INFRASTRUCTURE & SECURITY IMPLEMENTATION
Page 2/16
Firewall & Proxy:
  Strict Zoning Rules: Segmentation between LAN - DMZ - WAN.
  NAT Configuration: Enable Internet access for internal networks.
  HAProxy: Reverse Proxy & SSL Offloading for internal server protection.
2. Security with pfSense & Suricata IPS:
Page 8/16
Faculty of Computer Engineering and Electronics
Intrusion Prevention (Suricata):
  Mode: IPS (Legacy Mode) – Inline traffic inspection.
  Action: Automatically Drop Packet & Block Offenders based on ETOpen rulesets.

## Slide 9
6. MONITORING SYSTEM IMPLEMENTATION (PLG STACK)
Page 2/16
Faculty of Computer Engineering and Electronics
Docker Compose Architecture:
  5 Containers: Prometheus, Alertmanager, Loki, Promtail, Grafana.
Observability Capabilities:
  Network: Bandwidth usage, Port status (UP/DOWN).
  System: Server resources (CPU, RAM, Disk).
  Logs: Centralized Syslog from Cisco, pfSense, Nginx.
Alerting:
  Channel: Telegram.
  Triggers: Port Down, High Latency, Backup Failed.
Faculty of Computer Engineering and Electronics
Page 9/18

## Slide 10
7. AUTOMATION IMPLEMENTATION (ANSIBLE & TELEPORT)
Page 2/16
Faculty of Computer Engineering and Electronics
Faculty of Computer Engineering and Electronics
1. Ansible Playbooks:
  switch_backup.yml: Automates periodic configuration backups for Cisco Switches.
  pfsense_backup.yml: Retrieves and backs up pfSense XML configuration files.
  teleport-automation.yml: Auto-provisions Teleport Agents for secure remote access.
  Tool Installation: Automated deployment of essential tools (Docker, Node Exporter, Promtail) ensuring environment consistency.
2. Provisioning & Deployment:
Page 10/18

## Slide 11
7. AUTOMATION IMPLEMENTATION (ANSIBLE & TELEPORT)
Page 2/16
Faculty of Computer Engineering and Electronics
Faculty of Computer Engineering and Electronics
Access Management with Teleport:
  Replaces traditional SSH Keys (reducing security risks).
  Session-based access control.
  Audit Log: Records all administrator commands and sessions.
Page 11/18

## Slide 12
8. EXPERIMENTAL RESULTS
Page 2/16
Faculty of Computer Engineering and Electronics
Faculty of Computer Engineering and Electronics
1. Real-time Dashboard (Grafana):
  Centralized Dashboard: Visualizes network traffic and aggregated logs.
  Backup Status: Real-time tracking of backup completion and health.
  Traffic Visibility: Granular insights into traffic patterns and flows.
Page 12/18

## Slide 13
8. EXPERIMENTAL RESULTS
Page 2/16
Faculty of Computer Engineering and Electronics
Faculty of Computer Engineering and Electronics
2. Automation Capabilities:
  Scheduled Backups: Executes configuration backups precisely at 02:00 AM daily.
  Agent Provisioning: Automated setup of Teleport agents for all devices.
  Rapid Deployment: Quick installation and configuration of Docker environments.
Page 13/18

## Slide 14
8. EXPERIMENTAL RESULTS
Page 2/16
Faculty of Computer Engineering and Electronics
Faculty of Computer Engineering and Electronics
3. Automated Alerting & Reporting:
  Precision Alerting: Instant, accurate notifications triggered by system events.
  Daily Reporting: Automated PDF system health reports sent via Telegram.
Page 14/18

## Slide 15
8. EXPERIMENTAL RESULTS
Page 2/16
Faculty of Computer Engineering and Electronics
Faculty of Computer Engineering and Electronics
Page 15/18
4. Attack & Prevention Scenarios (Suricata):
  Nmap Scan: Suricata detects scan signature -> Blocks IP.
  DoS Attack (Hping3): Detects SYN Flood -> Drops connection.
  Result: Web remains accessible and stable.

## Slide 16
9. EVALUATION & FUTURE DEVELOPMENT
Page 2/16
Faculty of Computer Engineering and Electronics
Faculty of Computer Engineering and Electronics
Advantages:
  Comprehensive: Covers Administration - Monitoring - Security.
  Cost-effective: 100% Open Source software.
  Proactive: Fast incident response and resolution.
Limitations:
  Tested on Small/Medium scale (SMB).
  Defense capabilities require further tuning for large-scale attacks.
  Integrate AI/ML for Log Analysis (Anomaly Detection).
  Expand to Kubernetes Cluster for scalability.
Future Development:
Page 16/18

## Slide 17
10. CONCLUSION
Page 2/16
Faculty of Computer Engineering and Electronics
Faculty of Computer Engineering and Electronics
1. Technical Achievements:
  Successfully realized a comprehensive NetDevOps model.
  Stable operation across Automation, Monitoring, and Security layers.
2. Economic & Management Efficiency:
  Cost Optimization: No licensing fees (Open Source).
  Productivity: Reduced manual workload, eliminated human errors via Ansible.
3. Applicability:
  High feasibility for SMBs (Small and Medium-sized Businesses).
  Scalable Architecture: Modular design (Docker) allows for easy expansion.
Page 17/18

## Slide 18
Faculty of Computer Engineering and Electronics
Thank You!
Nhân bản – Phụng sự – Khai phóng
Page 18/18